## Slide 1
Ultrasonic Information Transfer
A Novel Approach to Wireless Communication
Presented by: Yoni Grinberg & Bar Harush
Supervisor: Dr. Elena Ravve
Team Code: 26-1-D-7

## Slide 2
What We Are Going To Do:
Ultrasonic Data Transfer
Our project uses ultrasonic waves for data transfer, leveraging their ability to propagate through liquids and be contained by solid barriers.
Cross-Platform Network
A many-to-many ultrasonic data transfer network for Android and iOS, with advanced collision avoidance.

## Slide 3
Why Ultrasound:
RF Challenges
Crowded frequency spectrums.
Susceptible to electromagnetic interference.
Signal congestion and "snooping" risks.
Poor propagation through conductive media (e.g., water, human body).
Ultrasound Advantages
Propagates well through liquids and tissue.
Naturally contained by solid barriers, enhancing security.
Avoids crowded radio spectrums.
Ideal for environments where RF fails (e.g., operating rooms, underwater).

## Slide 4
Why Is The Project Not Trivial?
From PoC to Network Layer: Transitioning from a basic one-to-one physical link to a robust, scalable many-to-many communication protocol.
Cross-Platform Interoperability: Achieving seamless data exchange between heterogeneous mobile operating systems (Android vs. iOS) with unique audio chipsets and hardware constraints.
Physical and Algorithmic Constraints: Managing severe acoustic challenges like Multipath Propagation (echoes) and Self-Interference on non-real-time mobile hardware.

## Slide 5
Project Objectives
Bridging the Gap
From basic acoustic links to a robust, scalable, and secure network layer.
Secure Multi-User Network
Establish a secure, multi-user ultrasonic network for non-RF applications.
Advanced Arbitration
Implement CSMA/CA for sophisticated channel arbitration.
Cross-Platform Compatibility
Ensure seamless operation between Android and iOS devices.

## Slide 6
Algorithmic challenges and solutions:
Mitigating Acoustic Interference and Noise
Challenge: Indoor environments suffer from severe Multipath Propagation, where sound echoes overlap and cause Inter-Symbol Interference (ISI).
Solution: Implementing a conservative 0.5ms bit duration to allow signal echoes to decay and utilizing Frequency-Shift Keying (FSK) for robust signal modulation.
Decentralized Channel Arbitration
Challenge: Managing many-to-many communication without a central server or global clock.
Solution: Developing a CSMA/CA-based protocol using unique, prime-number-based backoff timers to minimize collision probability.

## Slide 7
Algorithmic challenges and solutions: (cnt.)
Overcoming the Hidden Node Problem
Challenge: Undetectable collisions occurring when two transmitters, out of range of each other, simultaneously signal a central receiver.
Solution: Utilizing a synchronized RTS/CTS (Request to Send / Clear to Send) handshake to logically reserve the medium at the receiver's end.
Ensuring Data Integrity in Noisy Channels
Challenge: Environmental noise can easily flip bits in a 160-bit frame.
Solution: Implementing a robust 16-bit CRC checksum and an ACK/NACK feedback loop to verify and retransmit corrupted packets.

## Slide 8
Building on Prior Work
Our project advances previous research in ultrasonic data transfer.
1
Foundational PoC
Previous teams established a one-to-one ultrasonic communication channel between two Android devices.
2
Physical Layer
Utilized Frequency-Shift Keying (FSK) for acoustic data transfer.
3
Frequency Selection
Determined 18-19 kHz as optimal for inaudible mobile communication.
4
Data Processing
Implemented Fast Fourier Transform (FFT) for decoding binary data.

## Slide 9
Hardware Equipment:
Heterogeneous Mobile Nodes (Receivers/Transmitters):
We require at least three concurrent devices to validate the many-to-many network topology and collision avoidance.
Testing must include a variety of models—specifically two Android devices and one iPhone—to account for different audio chipsets and microphone placements.
Cross-Platform Development and Compilation:
An Apple Mac is an essential requirement for utilizing the iOS development environment and compiling code for the iPhone Operating System.
Development relies on standard Android and iOS APIs, specifically AudioTrack/AudioRecord for Android and AVAudioEngine for iOS.

## Slide 10
Hardware Equipment: (cnt.)
Testing Environment Tools:
Access to standard physical obstacles (e.g., solid barriers and walls) is necessary to verify the signal containment and security properties of ultrasonic waves .
Professional audio analysis software (e.g., Audacity) is required to verify that bit durations precisely meet the 0.5ms timing requirement .

## Slide 11
Addressing Previous Limitations
Past Challenges
Lack of Network Protocol: Limited to one-to-one connections, unable to handle multiple devices simultaneously. Collisions occurred with three or more devices.
Single Platform Restriction: Exclusively Android, limiting real-world application with heterogeneous devices (Android and iOS).
Our Impdrovements
Many-to-Many Communication: Introducing CSMA/CA for sophisticated channel arbitration.
Cross-Platform Compatibility: Ensuring seamless operation between Android and iOS.

## Slide 12
What Is Our Approach? Frequency-Shift Keying algorithm
Protocol Overview & Parameters
We utilize a multi-layered acoustic communication protocol designed for secure, many-to-many data transfer in non-RF environments.
Physical Layer: Frequency-Shift Keying (FSK) modulation utilizing high-frequency carrier waves (18–20 kHz) to ensure inaudibility.
Data Link Layer: A decentralized CSMA/CA arbitration mechanism with an RTS/CTS handshake to mitigate the Hidden Node Problem.
Protocol Inputs:
  UserID — 40-bit unique sender identifier.
  Sequence Number — 8-bit packet order identifier.
  Payload — 88-bit user message data.
Protocol Output:
  Modulated Waveform — FSK-encoded ultrasonic audio stream.
Algorithm (pseudo code)
Function TransmitSignal(bitStream):
track = InitAudioTrack(SAMPLE_RATE) for each bit in bitStream:
if bit == 0
then targetFreq = 18000 HZ
else targetFreq = 20000
end if
buffer = GenerateSineWave(targetFreq, phase) ApplyAmplitudeRamp(buffer)
track.write(buffer)end for track.stop()End Function

## Slide 13
Mechanism: We implement a decentralized, asynchronous "Listen-Before-Talk" principle to manage many-to-many communication without a central server.
Collision Avoidance: Utilizing an RTS/CTS (Request to Send / Clear to Send) handshake to logically reserve the acoustic medium and solve the Hidden Node Problem.
Backoff Strategy: We use unique prime-number-based timers to minimize the probability of simultaneous retransmissions.
Protocol Inputs:
RBWP — Regular Base Waiting Period (high prime number).
MBWP — Minimal Base Waiting Period (low prime number fallback).
Channel State — Real-time detection of 18–20 kHz activity.
Protocol Outputs:
RTS/CTS Frames — 56-bit control signals for medium reservation.
ACK/NACK — Confirmation or error signals for frame integrity.
Function ExecuteCSMA(payload):
while True:
wait for RBWP_Timer to expire
if ChannelIsIdle(18-20kHz)
then Transmit(RTS_Frame)
wait for CTS_Frame (Timeout = 2s)
if CTS_Received
then Transmit(Data_Frame)
wait for ACK
return Success
else
wait MBWP (Random Backoff)
end if
else
wait MBWP until idle
end if
end while
End Function
Our Approach – Carrier Sense Multiple Access/Collision Avoidance

## Slide 14
Why Carrier Sense Multiple Access
/Collision Avoidance
Works
Collision Avoidance
CSMA/CA verifies channel availability before transmission, preventing signal collisions and packet loss.
Cross-Platform Compatibility
Robust frameworks exist for standardized Digital Signal Processing (DSP) and uniform hardware access.
Resilience to Dynamic Topology
Decentralized and asynchronous, allowing devices to join or leave instantly without network stalls.
Asynchronous Operation
"Listen-Before-Talk" principle is robust for devices with varying OS delays, unlike strict time synchronization.
Hidden Node Solution (RTS/CTS)
Explicitly reserves the medium at the receiver's end, ensuring all nodes know the channel is busy.

## Slide 15
Implementation: Data Encoding – Frequency-Shift Keying
Our application uses FSK to encode binary data onto ultrasonic sound waves. This digital modulation technique changes the frequency of a carrier signal to transmit information.
Binary FSK (BFSK): Carrier shifts between two discrete frequencies for binary (0s and 1s) information.
Frequency Selection: 18 kHz for '0' and 20 kHz for '1', inaudible to humans.
Bit Duration: Optimal 0.5 milliseconds per bit, allowing for signal stability and receiver sampling.

## Slide 16
Implementation: Connection Establishment Request to Send / Clear to Send
1
RTS (Request to Send)
Transmitter sends a short control frame indicating intent to transmit and occupy the medium.
2
Wait (SIFS)
Transmitter listens for a predefined window (Timeout).
3
CTS (Clear to Send)
If the receiver is idle, it responds with a CTS frame, informing other participants the channel is busy.
4
Data Transmission
Upon receiving CTS, the transmitter sends the full data packet.
5
Acknowledgement (ACK)
Receiver sends ACK upon correct data arrival; sender retransmits if no ACK.

## Slide 17
Use Case: Many-to-Many Interaction and Messaging Protocol

## Slide 18
Class Diagram: Structural Design of the CSMA/CA and Signal Processing Layers

## Slide 19
Expected Results & Key Specifications
Fully Functional Network
Acoustic communication network using ultrasonic waves.
Cross-Platform
Seamless communication between Android and iOS devices.
Reliable Protocol
Data Link Layer with RTS/CTS collision avoidance.
Capacity & Range
Supports 3+ concurrent nodes within a 2-meter radius.
Many-to-Many Topology
Manages data transfer from multiple emitters to multiple recipients.

## Slide 20
Sequence Diagram: CSMA/CA Protocol with RTS/CTS Handshake Sequence

## Slide 21
Activity Diagram: CSMA/CA Protocol with RTS/CTS Handshake

## Slide 22
Sequence Diagram – Data Transmission and Frame Verification Protocol

## Slide 23
Activity Diagram: Data Framing and Physical Layer