## Slide 1
Ultrasonic Information Transfer
Application for Information Transfer Using Ultrasound Waves
Presented by: Yoni Grinberg 307868257 & Bar Harush 205713308
Supervisor: Dr. Elena Ravve
Team Code: 26-1-D-7

## Slide 2
What We Are Going To Do:
Ultrasonic Data Transfer
Our project uses ultrasonic waves for data transfer, leveraging their ability to propagate through liquids and be contained by solid barriers.
Cross-Platform Network
A many-to-many ultrasonic data transfer network for Android and IOS, with advanced collision avoidance.

## Slide 3
Why Ultrasound:
RF Challenges
Crowded frequency spectrums.
Susceptible to electromagnetic interference.
Signal congestion and "snooping" risks.
Poor propagation through conductive media (examples: water, human body).
Ultrasound Advantages
Propagates well through liquids and tissue.
Naturally contained by solid barriers, enhancing security.
Avoids crowded radio spectrums.
Ideal for environments where RF fails (examples: operating rooms, underwater).

## Slide 4
Why Is The Project Not Trivial?
From PoC to Network Layer: Transitioning from a basic one-to-one physical link to a robust, scalable many-to-many communication protocol.
Cross-Platform Interoperability: Achieving seamless data exchange between heterogeneous mobile operating systems (Android vs. IOS) with unique audio chipsets and hardware constraints.
Physical and Algorithmic Constraints: Managing severe acoustic challenges like Multipath Propagation (echoes) and Self-Interference on non-real-time mobile hardware.

## Slide 5
Project Objectives:
Bridging the Gap
From basic acoustic links to a robust, scalable, and secure network layer.
Secure Multi-User Network
Establish a secure, multi-user ultrasonic network for non-RF applications.
Advanced Arbitration
Implement Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA) for sophisticated channel arbitration.
Cross-Platform Compatibility
Ensure seamless operation between Android and IOS devices.

## Slide 6
Algorithmic Challenges And Solutions:
Mitigating Acoustic Interference and Noise
Challenge: Indoor environments suffer from severe Multipath Propagation, where sound echoes overlap and cause Inter-Symbol Interference (ISI).
Solution: Implementing a conservative 0.5ms bit duration to allow signal echoes to decay and utilizing Frequency-Shift Keying (FSK) for robust signal modulation.
Decentralized Channel Arbitration
Challenge: Managing many-to-many communication without a central server or global clock.
Solution: Developing a CSMA/CA-based protocol using unique, prime-number-based backoff timers to minimize collision probability.

## Slide 7
Algorithmic Challenges And Solutions: (cnt.)
Overcoming the Hidden Node Problem
Challenge: Undetectable collisions occurring when two transmitters, out of range of each other, simultaneously signal a central receiver.
Solution: Utilizing a synchronized RTS/CTS (Request to Send / Clear to Send) handshake to logically reserve the medium at the receiver's end.
Ensuring Data Integrity in Noisy Channels
Challenge: Environmental noise can easily flip bits in a bit frame.
Solution: Implementing a robust 8-bit CRC checksum and an ACK/NACK feedback loop to verify and retransmit corrupted packets.

## Slide 8
Building on Prior Work:
Our project advances previous research in ultrasonic data transfer.
1
Foundational PoC
Previous teams established a one-to-one ultrasonic communication channel between two Android devices.
2
Physical Layer
Utilized Frequency-Shift Keying (FSK) for acoustic data transfer.
3
Frequency Selection
Determined 18-19 kHz as optimal for inaudible mobile communication.
4
Data Processing
Implemented Fast Fourier Transform (FFT) for decoding binary data.

## Slide 9
Hardware Equipment:
Heterogeneous Mobile Nodes (Receivers/Transmitters):
We require at least three concurrent devices to validate the many-to-many network topology and collision avoidance.
Testing must include a variety of models—specifically two Android devices and one iPhone—to account for different audio chipsets and microphone placements.
Cross-Platform Development and Compilation:
An Apple Mac is an essential requirement for utilizing the IOS development environment and compiling code for the iPhone Operating System.
Development relies on standard Android and IOS APIs, specifically AudioTrack/AudioRecord for Android and AVAudioEngine for IOS.

## Slide 10
Hardware Equipment: (cnt.)
Testing Environment Tools:
Access to standard physical obstacles (examples: solid barriers and walls) is necessary to verify the signal containment and security properties of ultrasonic waves .
Professional audio analysis software is required to verify that bit durations precisely meet the 0.5ms timing requirement .

## Slide 11
Addressing Previous Limitations:
Past Challenges
Lack of Network Protocol: Limited to one-to-one connections, unable to handle multiple devices simultaneously. Collisions occurred with three or more devices.
Single Platform Restriction: Exclusively Android, limiting real-world application with heterogeneous devices (Android and IOS).
Our Improvements
Many-to-Many Communication: Introducing CSMA/CA for sophisticated channel arbitration.
Cross-Platform Compatibility: Ensuring seamless operation between Android and IOS.

## Slide 12
Our Approach – Frequency-Shift Keying Algorithm
Protocol Overview & Parameters
We utilize a multi-layered acoustic communication protocol designed for secure, many-to-many data transfer in non-RF environments.
Physical Layer: Frequency-Shift Keying (FSK) modulation utilizing high-frequency carrier waves (18–20 kHz) to ensure inaudibility.
Data Link Layer: A decentralized CSMA/CA arbitration mechanism with an RTS/CTS handshake to mitigate the Hidden Node Problem.
Protocol Inputs:
  UserID/Payload — 40-bit unique sender identifier.
  Starting and Separating Character— 8-bit.
  CheckSum — 8-bit.
Protocol Output:
  Modulated Waveform — FSK-encoded ultrasonic audio stream.
Algorithm (pseudo code)
Function TransmitSignal(bitStream):
track = InitAudioTrack(SAMPLE_RATE) for each bit in bitStream:
if bit == 0
then targetFreq = 18000 HZ
else targetFreq = 20000
end if
buffer = GenerateSineWave(targetFreq, phase) ApplyAmplitudeRamp(buffer)
track.write(buffer) end for track.stop() End Function

## Slide 13
Implementation: Data Encoding – Frequency-Shift Keying
Our application uses FSK to encode binary data onto ultrasonic sound waves. This digital modulation technique changes the frequency of a carrier signal to transmit information.
Binary FSK (BFSK): Carrier shifts between two discrete frequencies for binary (0s and 1s) information.
Frequency Selection: 18 kHz for '0' and 20 kHz for '1', inaudible to humans.
Bit Duration: Optimal 0.5 milliseconds per bit, allowing for signal stability and receiver sampling.

## Slide 14
Mechanism: We implement a decentralized, asynchronous "Listen-Before-Talk" principle to manage many-to-many communication without a central server.
Collision Avoidance: Utilizing an RTS/CTS (Request to Send / Clear to Send) handshake to logically reserve the acoustic medium and solve the Hidden Node Problem.
Backoff Strategy: We use unique prime-number-based timers to minimize the probability of simultaneous retransmissions.
Protocol Inputs:
RBWP — Regular Base Waiting Period (high prime number).
MBWP — Minimal Base Waiting Period (low prime number fallback).
Channel State — Real-time detection of 18–20 kHz activity.
Protocol Outputs:
RTS/CTS Frames — 56-bit control signals for medium reservation.
ACK/NACK — Confirmation or error signals for frame integrity.
Function ExecuteCSMA(payload):
while True:
wait for RBWP_Timer to expire
if ChannelIsIdle(18-20kHz)
then Transmit(RTS_Frame)
wait for CTS_Frame (Timeout = 2s)
if CTS_Received
then Transmit(Data_Frame)
wait for ACK
return Success
else
wait MBWP (Random Backoff)
end if
else
wait MBWP until idle
end if
end while
End Function
Our Approach – Carrier Sense Multiple Access/Collision Avoidance

## Slide 15
Why Carrier Sense Multiple Access
/Collision Avoidance works:
Collision Avoidance
CSMA/CA verifies channel availability before transmission, preventing signal collisions and packet loss.
Cross-Platform Compatibility
Robust frameworks exist for standardized Digital Signal Processing (DSP) and uniform hardware access.
Resilience to Dynamic Topology
Decentralized and asynchronous, allowing devices to join or leave instantly without network stalls.
Asynchronous Operation
"Listen-Before-Talk" principle is robust for devices with varying OS delays, unlike strict time synchronization.
Hidden Node Solution (RTS/CTS)
Explicitly reserves the medium at the receiver's end, ensuring all nodes know the channel is busy.

## Slide 16
Implementation: Connection Establishment Request to Send / Clear to Send
1
RTS (Request to Send)
Transmitter sends a short control frame indicating intent to transmit and occupy the medium.
2
Wait (SIFS)
Transmitter listens for a predefined window (Timeout).
3
CTS (Clear to Send)
If the receiver is idle, it responds with a CTS frame, informing other participants the channel is busy.
4
Data Transmission
Upon receiving CTS, the transmitter sends the full data packet.
5
Acknowledgement (ACK)
Receiver sends ACK upon correct data arrival; sender retransmits if no ACK.

## Slide 17
Expected Results & Key Specifications:
Fully Functional Network
Acoustic communication network using ultrasonic waves.
Cross-Platform
Seamless communication between Android and IOS devices.
Reliable Protocol
Data Link Layer with RTS/CTS collision avoidance.
Capacity & Range
Supports 3+ concurrent nodes within a 2-meter radius.
Many-to-Many Topology
Manages data transfer from multiple emitters to multiple recipients.

## Slide 18
Use Case: Many-to-Many Interaction and Messaging Protocol

## Slide 19
Class Diagram: Structural Design of the CSMA/CA and Signal Processing Layers

## Slide 20
Comprehensive Testing of Embedded Communication:
This section presents the testing methodologies used to validate the functionality, integrity, and robustness of the embedded communication stack. It covers bit-level operations, physical layer characteristics, system integration, and real-world performance under various conditions.

## Slide 21: Unit Testing: Bit Packing & Fragmentation Logic
1
Objective
Verify the ConstructPacket function accurately packs "Total Packets" and "Current Index" into a single byte.
2
Procedure
Input Total=3, Index=2. Execute the bit-packing logic.
3
Success Criteria
The resulting byte must be 0x32 (Binary 00110010).

## Slide 22
Objective
Validate the integrity of the CRC checksum algorithm used within the communication stack.
Procedure
Manually calculate the CRC sum for the string "TEST". Then, run the code's dedicated checksum function on the identical string.
Success Criteria
The output from the code's checksum function must precisely match the pre-calculated manual CRC sum.
1
2
3
Unit Testing: Checksum Calculation Accuracy

## Slide 23
Objective
Ensuring the raw string payload is correctly transformed into the binary protocol frame according to strict ordering requirements.
Procedure
Pass the string "TEST" into the serializer function. Inspect the generated output bit array.
Success Criteria
The bit array must rigidly adhere to the defined frame structure: Preamble -> Sync -> Frag -> Length -> Payload -> Checksum.
1
2
3
Unit Testing: Packet Serialization

## Slide 24
Objective
Test the FFT logic using a mathematically generated array to ensure precise frequency detection.
Procedure
Feed an array containing a pure mathematical sine wave of 18kHz into the detection function.
Success Criteria
The algorithm must return a significantly higher magnitude for the 18kHz bin when compared to the 20kHz bin.
1
2
3
Unit Testing: Frequency Analysis Algorithm
Notes: Testing the Fast Fourier Transform (FFT) logic for accurate frequency component detection using controlled input

## Slide 25
Objective
Confirm that each transmitted bit maintains an exact duration of 0.5ms, as specified by the protocol.
Procedure
Record the transmission of a single bit using an external PC equipped with audio editing software (e.g., Audacity). Measure the precise length of the recorded waveform.
Success Criteria
The measured waveform duration must be exactly 0.5ms, demonstrating accurate bit timing.
1
2
3
Physical Layer Testing: Bit Duration and Timing

## Slide 26
Objective
Test the successful end-to-end transfer of a short message between devices.
Procedure
The transmitting (Tx) device sends the string "TEST" to the receiving (Rx) device.
Success Criteria
The Rx device correctly decodes the message, checksum validation passes, and the text "TEST" is displayed on the screen.
1
2
3
Integration Testing: Single Packet Transmission

## Slide 27
Objective
Ensure the collision avoidance mechanism (Request To Send/Clear To Send) functions as expected.
Procedure
The Tx device initiates a transmission sequence.
Success Criteria
Tx waits for CTS. Rx sends CTS upon hearing RTS. Tx only transmits data after receiving CTS.
1
2
3
Integration Testing: RTS/CTS Handshake

## Slide 28
Objective
Determine the maximum reliable communication distance.
Procedure
Place devices 10cm apart; increase distance by 10cm until decoding fails.
Success Criteria
Document the precise distance at which reliable communication ceases.
1
2
3
Field Testing: Maximum Effective Range

## Slide 29
Objective
Validate system performance in a noisy environment.
Procedure
Perform transmission while introducing external noise near the receiver.
Success Criteria
The system must successfully filter external noise and maintain communication integrity.
1
2
3
Field Testing: Noise Immunity

## Slide 30
Verifying the signal's ability to diffract around or penetrate obstacles, determining if direct Line-of-Sight (LOS) is mandatory for effective communication.
1
Step 1: Baseline
Establish a stable connection between devices at a distance of 2 metres.
2
Step 2: Level 1 Obstacle
Introduce a sheet of paper directly between the speaker and microphone.
3
Step 3: Level 2 Obstacle
Introduce a human body as an obstacle.
4
Step 4: Level 3 Obstacle
Introduce a solid wooden door or wall.
Success Criteria: Pass
The system must accurately report signal loss or checksum failure when the signal is blocked. It must not crash or display random garbage data.
Field Testing: Wall/Barrier Penetration Test
Notes: Verifying the signal's ability to diffract around or penetrate obstacles, determining if direct Line-of-Sight (LOS) is mandatory for effective communication.

## Slide 31
Objective
Ensure the application does not crash or overheat during continuous operation.
Procedure
Run a continuous transmission loop for a minimum duration of 10 minutes.
Success Criteria
The application must remain stable throughout the test, with no "Application Not Responding" errors or unexpected terminations.
1
2
3
Field Testing: Battery and Thermal Stability
Notes: Ensuring the application maintains operational integrity and optimal temperature during prolonged, continuous use

## Slide 32
Thank You for Listening!

## Slide 33
Sequence Diagram: CSMA/CA Protocol with RTS/CTS Handshake Sequence

## Slide 34
Activity Diagram: CSMA/CA Protocol with RTS/CTS Handshake

## Slide 35
Sequence Diagram – Data Transmission and Frame Verification Protocol

## Slide 36
Activity Diagram: Data Framing and Physical Layer